## Table of contents
- kernel space / user space communication (part I?)
  - sysfs
  - ioctl
  - netlink / genetlink (not to be discussed in details)
  - driver memory mapping (not to be discussed in details)
  - AIO (not to be discussed in details - because I know no one who knows this)
  - Labs:
- Device Drivers:
  - Basic device-driver purpose (allow use of some HW peripherial)
  - Driver basic ’functionalities’
- Device-tree / driver model
  - Driver model:
- SystemD
- Networking
## kernel space / user space communication (part I?)
Including some of the following:
### sysfs
- Current "de facto" control interface - preferred over ioctl
- Filesystem based interface
  - Allows easy-to-access interface to driver
  - Models the HW architecture in folder structure.
- show & store callcbacks.(read/write)
- usually meant to be plain text files but binary files are also supported
Sysfs internals shortly (not required for using sysfs)
Every directoty in sysfs is a kobject and files in directory are the attributes.
- kobjects:
  - are objects of type strcuct kobject
  - provide reference counting
    - kobject_get() kobject_put()
    - When reference count reaches zero, release is called from struct kobj_type. This should perform appropriate cleanup
    - kobj_type also contains information about kobjects sysfs representation. (for binary files this is somewhat different)
      - (see file adding: http://lxr.free-electrons.com/source/fs/sysfs/file.c?v=4.3#L238 )
    - kobjects are grouped into ksets
- https://www.kernel.org/doc/Documentation/kobject.txt
- attributes:
  - Attributes provide a file in sysfs.
    - struct attribute defines the name and mode of file
- For callbacks we need xxx_attr struct depending on use case
  - Usually expect ASCII text to be read/written - struct kobj_attribute, struct device_attribute, struct bus_attribute, struct driver_attribute
  - For binary files: struct bin_attribute
  - Note to self: https://lwn.net/Articles/31220/  - test the comment by Alan Stern
https://www.kernel.org/doc/Documentation/filesystems/sysfs.txt
Example code and explanations.
PROs
  - Simple for user space
  - Easy access from shell
CONs
  - Not quite as lightweight as ioctl.
  - Binary file support separate from ASCII file support
  - Not quite as simple from driver perspective as ioctl
### ioctl
- "Old" communication channel. Still heavily used.
- Only one multi purpose device file in user space.
- int ioctl(int fd, int request, ...)
  - request parameter specifies operation.
  - third argument typically a pointer to data.
- usable with character devices, misc devices, block devices...
- driver fills the file_operation struct and registers it to kernel.
- register_chrdev, misc_register, ...
- Userspace opens device file and calls ioctl
=> unlocked_ioctl or compat_ioctl called from driver.
- in driver the request is differentiated by 'request' parameter.
- Request numbers are to be constructed using _IO* macros
  - http://lxr.free-electrons.com/source/include/uapi/asm-generic/ioctl.h?v=4.3#L78
  - http://lxr.free-electrons.com/source/Documentation/ioctl/ioctl-number.txt?v=4.3
PROs
  - Should be pretty lightweight (I've no numbers but some Ulm colleague did some perf tests)
  - Driver side is really simple
CONs
  - Sysfs is preferred by community.
  - Not so simple for user, request conflicts.
### netlink / genetlink (not to be discussed in details)
- Widely used in networking subsystem
- based on a clien-server model
- userspace library (libnl)
  - https://www.infradead.org/~tgr/libnl/doc/core.html
- Typically used to transfer buffers with TLV data.
- Provides good facilities for parsing TLV buffers.
#### Netlink
- socket(PF_NETLINK, socket_type, netlink_family (kind of protocol))
- Predefined protocol numbers - limited to 32 in total.
#### Generic netlink
- Built on top of netlink
- Has own specific netlink protocol number (family)
- Adds dynamic (generic)netlink family allocation
  - Drivers can register families to generic netlink controller
  - Families have name and they will be queried at runtime from generic netlink controller by clients.
PROs
  - Natural support for having multiple (userspace) clients.
  - multicasts
  - well suited for generating events from driver
  - Flexible
CONs
  - Not-so-easy user space applications
  - Amount of existing documentation (not so much for framework but for existing use-cases like rtnetlink)
Simple example about netlink.
generic_netlink.cnetlink_training.hnetlink_user.c
### driver memory mapping (not to be discussed in details)
PROs
  - No system call required => as fast as it can be.
CONs
  - Do it all yourself approach.
Example piece of code with ioctl and memory mapping:
ioctl_test.cioctl_test_user.c
### AIO (not to be discussed in details - because I know no one who knows this)
If someone is able to explain the AIO framework - please let us know.
PROs
Many simultaneous I/O requests ongoing even with non multithreaded application (SSD chips for example)
CONs
- Sub optimal interface judging the LWN article
- Lack of documentation
http://lwn.net/Articles/671649/
### Labs:
#### Lab1 - familiarize yourself with sysfs structure and basic mechanisms
Create a module which creates a class device with 3 sysfs files. You can use module from previous lab as basis.
- One of which can be read and written
- One which can be only read
- One which can be only written
In init function use:
class_register()
device_create() or
device_create_with_groups()
#### Lab2 - Oh, there is plenty of 'convenience things' in sysfs
See how filling class_attrs member in struct class (http://lxr.free-electrons.com/source/include/linux/device.h?v=4.3#L383) impacts by filling it prior to call to class_register.
#### Lab3 - basic ioctl fileops
Create a misc driver and fill open, close and ioctl operations. You can modify following user space program for testing it.
ioctl_test_user_no_mmap.c

#### Lab4 - reinventing the wheel
Modify memory mapping example so that
- Driver updates at least 128 bit data (struct with two 64bit values for example) in memory
- userspace program could reliably read the data from driver memory (no race condition)
## Device Drivers:
### Basic device-driver purpose (allow use of some HW peripherial)
- interrupts
- register access
### Driver basic ’functionalities’
- Initialization
  - register driver to kernel
  - HW-verification
  - HW/driver initialization (device-tree reading, ioremap, interrupt initialization, register access)
  - preparing userspace - kernelspace communizcation facilities (sysfs?)
  - preparing driver internal data
- Autonomous operation
  - interrupt handling (interrupt context specific caveats)
  - events to userspace (syfs_notify/netlink?)
- Serving user requests
  - typical race conditions (protected read-modify-write access to registers, memory barriers on SMB)
  - copy_to_user, copy_from_user?
  - generic dependency/policy issues – no userspace dependencies in kernel!
## Device-tree / driver model

- Device-tree purpose
  - describe HW
  - other options (?)
- Device-tree structure
  - go through example device-tree
- Obtaining device-tree information in kernel
  - set of of_xxx functions for retrieving data
  - of_xxx function for searching a node
  - of_node_put/of_node_get
  - for_each_xxx
- Compatible property!
- Binding documents
### Driver model:
- buses/drivers and how that binds to device-tree (bus code walks through own dt and instantiates found devices && calls probe for registered drivers)
- How bus/driver ‘hierarchy’ is reflected in sysfs.